## Slide 1: The Effect of Tailings Characteristics on Cover System Success (or: What have we learned in 40 years?)
Monisha Banerjee
Michael Milczarek Jason Keller
Tzung-mow Yao
Meg Buchanan
Thanks to Freeport McMoRan, BHP Billiton, ASARCO

## Slide 2: Physical, Geochemical and Spatial Tailings Characteristics

## Slide 3: Physical Characteristics
Tailings are poorly graded
  Mostly silt size
  No soil structure
  Highly erosive (high intensity precipitation/wind)
Impoundment construction results in additional sorting and layering
  beach (sands)
  slimes (silts)
  mixed areas
Moisture retention and permeability varies by material types
Variable saturation and drainage

## Slide 4: Tailings Segregation and Structure
Slimes (silt)
Beach (sand)
Mixed
Zone
(sand & silt)

## Slide 5: Geochemical Characteristics
Can be moderately saline to hyper-saline
Ore body mineralogy can result in:
  High acid generation potential (and acidity) with high plant available metals (i.e. arsenic)
  Moderate salts with no/ low plant-available metal content
Typically low plant nutrient content
Lack of organic matter and microbiota

## Slide 6: To Cap or Not To Cap?

## Slide 7: Reclamation Goals and Methods
Goals:
Establish vegetation
Minimize erosion and stabilize tailings
Minimize deep percolation
Methods:
Soil covers
Direct revegetation w/
tailings amendments

## Slide 8: Previously Reclaimed Tailings Surfaces (in AZ)
ASARCO Mission Tailings No. 6 (1983: 12-inch cover)
ASARCO Mission San Xavier Tailings 1,2, 3 (2011: 12 inch cover)
Eagle Pitcher Mill site (1960s, 1989-92: 12-inch cover)
Twin Buttes Tailing No. 2 (1986: 12-inch cover)
Phelps Dodge Sierrita Esperanza Tailings (1986: 12-inch cover)
San Manuel PS Tailings Impoundment 1/2 (1991-92: 6 to 8 inches cover)
San Manuel Tailing Impoundments 1-6 (2008: 12-inch cover)
San Manuel PS experimental biosolid plots (1998: no cover)
McCabe Mine Tailings (1996: 24 inch cover)
Phelps Dodge Morenci Tailings 4W experimental test plots (1997: 12 to 24-inch of cover)
Freeport McMoran Copper Queen CTSA Tailings (2012: 24 inch cover)
Acid
Potentially Acid Generating
Circumneutral
Notes: All test plots were on side slopes. Website provided at end of presentation with link to more detailed pubs.

## Slide 9: Matrix Approach
Cover Depth

## Slide 10: Vegetation on Reclaimed Tailings

## Slide 11
ASARCO Mission Tailings
Notes: ROCK ARMOR PRESENTATION (JASON) AFTERNOON

## Slide 13
Vegetation in 2005
No cover. Biosolid/green waste amended
San Manuel
Circum-neutral
Mixed zone/ Slimes Tailings
Reclaimed in 1999

## Slide 14
Vegetation in 2005
30-cm cover, reseeding/mulching,
hand planting
San Manuel
Circum-neutral Tailings, Beach/Mixed
Reclaimed in 1999

## Slide 15
Vegetation in 2007
30-cm cover, reseeded,
21 ton/acre biosolids,
Morenci
Acid tailings, Side-slope
Reclaimed in 1998

## Slide 16
30 cm Cover vs. 60 cm Cover
Chart: Year
| 1999 | 2002 | 2005 | 2008
30 cm Cover | 0.48 | 0.21 | 0.18 | 0.46
60 cm Cover | 0.52 | 0.24 | 0.2 | 0.44

## Slide 17
Rooting Characteristics

## Slide 19: Vegetation Considerations
Rooting characteristics:
  Actively root into circum-neutral tailings
  Minor rooting into moderately acid tailings, primarily limited to cover and upper one foot of tailings
  Form dense root mat above cover/acid tailings contact
  Affected by tailings permeability
Vegetative success generally greater in mixed zone than in beach areas and slime areas
Vegetation characteristics varies with location (e.g. slimes vs. sands)

## Slide 20: Vegetation Considerations (cont’d)
Effect of cover depth
  Nominal differences in vegetative covers > 30 cm thick
  BUT native species perform better on thicker covers
Effect of organic amendments:
  Can successfully reclaim raw tailings with a biosolids/green waste (compost) mix
  Results in significantly greater mean vegetation cover; however, less species diversity
  In some cases, observed effects sustained for over 10 years
Side slopes may require rock armoring; only seeded cover material may not adequately stabilize slopes

## Slide 21: Low-pH and Saline Solution Migration into Monolayer Covers?

## Slide 22: Trench Sample Design
0
45
75
(cm)

## Slide 23: pH Profiles
Typically
Phytoxic

## Slide 24: EC Profiles

## Slide 25
Tailing/Cover Contact

## Slide 26: Acid and Salinity Migration Considerations
In a semi-arid environment salinity and acid migration observed in Southwest US environment to be limited to ≈ 15 cm above contact
Phytotoxic levels of pH and salinity in cover material generally absent ≈ 5 cm above contact
Increased migration above contact with decreased cover thickness (30 vs. 60 cm)
Acidity and salinity migration may be limited due to:
  Unsaturated hydraulic conductivities and upward flux rates greatly diminish with distance above the contact
  High calcium carbonate contents in the cover material can neutralize low-pH solution

## Slide 27: Infiltration/Net Percolation

## Slide 28: Calculated 1D Net Percolation Flux
Sensor Nest/Plot Location | Total Downward Flux (cm) | Annual Flux (cm/yr) | Annual Flux Rate (cm/s) | Estimated Flux as Percent of Precipitation
30 cm cover, low vegetation |  |  |  | 
Average (3 to 2 nests) | 3.23 | 0.37 | 1.16E-08 | 1.29%
Standard Deviation | 1.61 | 0.26 | 8.14E-09 | 1.04%
30 cm cover, high vegetation |  |  |  | 
Average (3 to 2 nests) | 0.84 | 0.12 | 3.80E-09 | 0.34%
Standard Deviation | 6.52 | 0.07 | 2.24E-09 | 0.30%
60 cm cover, low vegetation |  |  |  | 
Average (3 to 1 nest) | 4.20 | 0.55 | 1.74E-08 | 1.68%
Standard Deviation | 7.37 | 0.55 | 1.76E-08 | 1.35%
Average 60 cm cover, high vegetation |  |  |  | 
Average (3 to 2 nests) | 3.84 | 0.48 | 1.53E-08 | 1.53%
Standard Deviation | 3.10 | 0.29 | 9.13E-09 | 1.24%
Bare Tailings |  |  |  | 
Average (3 nests) | 0.17 | 0.02 | 6.56E-10 | 0.09%
Standard Deviation | 0.28 | 0.03 | 1.11E-09 | 0.16%
Shallower (30 cm) cover/ Lower permeability tailings
Low permeability bare tailings: > runoff, less infiltration
Deeper (60 cm) cover/ Higher permeability tailings

## Slide 29: Predicted Effect of Increasing Cover Thickness
Tailing sideslope
Tailing beach
Tailing slimes

## Slide 30: Net Percolation Considerations
Lower permeability tailings reduce net percolation
Increasing cover thickness can have less influence on net percolation than tailings characteristics
Shallow covers or direct reclaimed tailings can have less net percolation than deeper covers
Tailings are an integral part of store and release cover systems and their influence should be considered during cover design

## Slide 31: Conclusions
Circumneutral tailings can be revegetated with organic amendments (if available); net percolation may actually decrease because of low permeability material at surface
Low permeability tailings serve to slow down infiltration and retain water in cover; can have greater effect on net percolation than cover depth
Revegetation seed mixes should consider differences between sand and slimes area; deeper covers are better for native seed mixes
Cover system modeling should acknowledge ET depth into tailings
Upward acidity and salinity migration into monolayer covers may be limited

## Slide 32: THANK YOU! monisha@gsanalysis.com More information at http://www.gsanalysis.com/minepub.html