## Slide 1
Ten-Year Performance Evaluation of the Evapotranspiration Cover
at Barrick Goldstrike Mine’s AA Leach Pad
Mike Milczarek, Jason Keller, Margaret Buchanan, Bob Rice, Mike Yao, Gary Goodrich, Johnny Zhan
Thanks to Dale Hammermeister and Joe Vinson

## Slide 2: Background
Goldstrike Mine located in north-central Nevada
  Average precipitation = 11.7 in/yr (29.7 cm/yr): 1990-2011
  Primarily snow, December through May
AA Leach Pad
  HDPE lined gold heap leaching facility
  Operated from 1987 to 1999
  224 acres and 55 million tons of ROM leached ore
Estimates of natural groundwater recharge rates
  Function of elevation and precipitation
  Maxey-Eakin (1949) approximation – 3% to 5% of precipitation
Evapotranspiration (ET) cover designed and placed in 2000-2001

## Slide 3: Barrick Gold Closure Objectives

## Slide 4: Designing an ET Cover
ET Cover – Seasonal storage and release of soil water
Fall Soil is initially dry due to previous growing season

## Slide 5: Designing an ET Cover
ET Cover – Seasonal storage and release of soil water
2. Winter
Rain and snowmelt gradually infiltrates, increasing soil water

## Slide 6: Designing an ET Cover
ET Cover – Seasonal storage and release of soil water
3. Spring Net percolation is most likely in this season (April-June) after a wet winter

## Slide 7: Designing an ET Cover
ET Cover – Seasonal storage and release of soil water
4. Late Spring & Early Summer Temperature warms, and evapo-transpiration increases

## Slide 8: Designing an ET Cover
ET Cover – Seasonal storage and release of soil water
5. Late Summer Continued transpiration by vegetation removes stored soil water from root zone

## Slide 9: Designing an ET Cover
- Downward/upward flux rates are controlled by soil hydraulic properties and pressure potential gradients
Zero flux plane defines depth at which downward flux is occurring
Design Factors
- Cover should contain ample water-holding capacity (loams ideal)
An abrupt textural contrast from loams/silts to gravel/ sands may create capillary break
ZERO FLUX PLANE

## Slide 10: AA Pad Closure
ET Cover Design Parameters
  Minimize net percolation from meteoric water
  Promote vegetation growth
Borrow material: fine grained topsoil or valley fill deposits (Carlin silt)
  Unsaturated flow modeling predicted nominal changes in flux above a 4 foot ET cover
Four foot ET cover (3 ft to 5.5 ft), placed in 2000-2001

## Slide 11: AA Pad Cover Performance Monitoring
Soil cover monitoring stations (14)
  Soil water dynamics (water content, soil water pressure potential)
  In-situ and laboratory hydraulic property characterization
  Various monitoring locations to access solar aspect, slope location, proximity to runoff channels, cover material type
    East transect – Carlin Silt, east aspect
    West transect – Topsoil, north aspect
    South transects - Carlin Silt, south aspect
  Station installation 2001 (East and West) and 2005 (South)
Estimate net percolation:
  Use 1D Darcy approximation using pressure potential data and hydraulic properties from bottom two sensor locations

## Slide 13
Notes: Change to 3(H):1(V) slope angle

## Slide 14
Notes: Remove “commingled Carlin, Petroleum” etc. Replace with “Carlin Silt (AA Pad South)?. Change angle to 3(H):1(V)

## Slide 15: Sensor Installation

## Slide 16: Data Summary

## Slide 18: Vegetation Data

## Slide 19: Vegetation after 10 years
Ground Cover Type | Transect |  | 
 | East | South | West
Total Plant | 26% | 36% | 89%
Perennial | 24% | 31% | 88%
Shrub and Forb | 17% | 21% | 87%

## Slide 20
West Transect
East Transect

## Slide 21: Water Content Data

## Slide 22: East Transect Water Storage

## Slide 23: West Transect Water Storage

## Slide 24: Field Water Holding Capacity

## Slide 25: Pressure Potential Data

## Slide 26: West 2 Matric Potential
Chart: Date

## Slide 27: East 4 Matric Potential
Chart: Date
Increasing dryness

## Slide 28: Estimated Net Percolation Fluxes

## Slide 29: Estimated Cumulative Flux East Transect

## Slide 30: Estimated Cumulative Flux Channels

## Slide 31: Estimated Cumulative Flux West Transect

## Slide 32: Estimated Cumulative Flux South Transect

## Slide 33: Estimated Cumulative Flux South WFMs

## Slide 34: Summary of Monitoring Data
Average precipitation during monitoring period (2001-2011) was 13.6 in/yr (34.5 cm/yr)
  2004-2005 wettest year in 35 years (Elko, NV)
Estimated net percolation (from pressure potential monitoring data) as percent of annual precipitation:
  0.7% for topsoil and 1.5% for Carlin
  3.7% for Carlin channels
  Area weighted average ≈ 0.85%
Significantly higher estimated net percolation in channels, some evidence of downslope water accumulation
Average and dry years - little to no deep percolation
Observed ET and rooting from greater than 5 feet

## Slide 35: AA Pad drain-down
Chart: Date

## Slide 36: Conclusions
ET cover has sufficient water storage, variable
Majority of net percolation is episodic, channels are foci
Estimated net percolation is well below regional estimates of recharge
  Topsoil shows best performance, Carlin adequate
  Variable soil and vegetation characteristics, rooting is not limited to cover material
Generally good agreement between monitoring data and draindown data
Multiple years of monitoring necessary

## Slide 37
THANK YOU
More information at: http://www.gsanalysis.com/minepub.html

## Slide 38: Maxey-Eakin Estimated Recharge (White River Valley, NV, 1949)
Interpolated
Recharge Estimate Intervals

## Slide 39: Vegetation after 10 years
Ground Cover Type | Transect |  | 
 | East | South | West
Total Plant | 26% | 36% | 89%
Perennial | 24% | 31% | 88%
Shrub and Forb | 17% | 21% | 87%
Kochia prostrata
Kochia prostrata
Agropyron (Wheatgrasses)
Elymus cinereus (Great Basin Wildrye)
Poa (Bluegrasses)
Bromus tectorum(Cheatgrass)
Atriplex Canescens (4-wing saltbush)
Purshia Tridenta (Bitterbush)

## Slide 40: Estimated Net Percolation (Pressure Potential data)