## Slide 1: Predicting and Managing Waste Impacts through a Holistic and Life-of-mine Geomet Application
Karin Olson Hoal, JKTech Pty Ltd, Brisbane Australia and
Colorado School of Mines
John Jackson, JKTech Pty Ltd, Brisbane Australia
David Mulligan and Mansour Edraki, Centre for Mined Land Rehabilitation, Sustainable Minerals Institute, University of Queensland, Australia
U.S. EPA Hardrock Mining Conference:
Advancing Solutions for a New Legacy
April 4 2012

## Slide 2
University of Queensland

## Slide 3
Sustainable Minerals Institute

## Slide 5: JKTech Pty Ltd
Brisbane Perth Johannesburg Denver Santiago

## Slide 6: Mining: Challenges
Lower grade deposits
Increasingly inaccessible deposits
Higher operating costs
Higher energy costs
Critical water issues
Perceptions

## Slide 7: JKAurecon: The link to infrastructure
Mining: Drivers

## Slide 8: Energy
(The following slides are Taken from JKMRC/JKTech/CRCORE 2010 presentation)
6-7% Australia’s energy on comminution
Mining houses target of 10-20% reduction
BCS, June 2007. Mining industry energy bandwidth study. US Department of energy
Notes: Geomet – planning – characterisation impacts on energy eg

## Slide 9: Mining: Perceptions
On the Nature of Metals (De re metallica) 1556, by Georg Bauer (Georgius Agricola)
Lawrence Gipe, “Rosemont Copper Girl:, 2011
Notes: However, much of society sees the mining industry as an archaic, unnecessary and risky industry (this is particularly true in the US where I come from). It is true that as you look at Agricola you appreciate that not a lot has changed in 500 years: we dig, process, melt in much the same way. But we know the technological advancements have been significant.
Compare this image with the alternate message: that mining is a new-age industry that is risk adverse and value adding for society. This marketing approach has been working in Arizona, for example.

## Slide 10: Perceptions
2010 World Economic Forum Report Mining & Metals Scenarios to 2030:
“…not anticipate any technological breakthroughs that would transform key aspects of the industry such as operations, metals and mineral use or energy technologies” for 30 years..
Notes: Nevertheless, the message is not coming through. This World Economic Forum report on mining scenarios for 30 years explicitly assumes there will not be any significant technological breakthroughs in the industry.

## Slide 11: Life-of-mine geomet application
Value
Locked in variable ore relationships
Team-based approach
Integrate data sets
Operating cost reduction
Risk mitigation
through life of project
Mineralogy
Closure
Reclamation
Drilling
Core logging
Geochemistry
Assay
Materials
Attributes
Metallurgical
tests
Mine plan and
design
Operations
QA/QC
Piloting
Geological model
Characterisation
data sets
$ value

## Slide 12: New approaches
Reconcile extraction with sustainable practice
Operational state-of-the-art approaches to integrated extraction beneficiation and mineral processing
Effective prediction
Environmental and economic impacts

## Slide 13: Predict …. Plan …. Manage
PREDICT performance
Recognize variability and geological drivers
Model relationships among attributes
Interpolate throughout mineral deposit
PLAN proactively
Integrate into mine plan and scheduling
Reduce uncertainty
Improve performance
MANAGE impacts
Understand and control environmental consequences
Reduce overall project risk
Recognize financial value through NPV and IRR options

## Slide 14: Understanding the variability in the deposit: Identifying the drivers of mining and processing responses
Intrinsic Rock Properties
Defining Physical Control
Front end

## Slide 15
Proxies
Geology, Assays,Equotip, Sonic, NIR
Indices
RBTEx, GeMCi
Attributes
SPI, DWT, RBT

## Slide 16: Met tests for variability vs composites
GeM Ci test
Rotary Breakage Tester
JKFI and MSI

## Slide 17
Blasting variability for mill
SAG Mill
HPGR
Blasting scenarios

## Slide 18: Comminution variability by lithology
SAG Plant
HPGR Plant

## Slide 19: Spatial understanding
1cm x 1cm grid
(From AMIRA P843)
eg Equotip

## Slide 20: Spatial 3D domains
Grade
Distribution of lithology and facies
Distribution of weathering and alteration
Mineralogy
Structural – geotech
Spatial distribution of met variables
Sampling and analytical precision

## Slide 21
Gain spatial understanding of geological controls
Au assay
Au >40% locked in py
clay

## Slide 22: Planning: Attributes into Block Model
Each Model Cell to Contain
Intrinsic Rock Properties
Performance Attributes
Performance Parameters

## Slide 23: Predict …. Plan …. Manage
PREDICT process performance
Recognize variability and geological drivers
Model relationships among attributes
Interpolate throughout mineral deposit
PLAN proactively
Integrate into mine plan and scheduling
Reduce uncertainty
Improve performance
MANAGE impacts
Understand and control environmental consequences
Reduce overall project risk
Recognize financial value through NPV and IRR options

## Slide 24
Back end:
Variability and environmental impact
Acid rock drainage:
  Predict acid potential and neutralization potential
  mineralogy: total sulfides, carbonates, silicates
Metal deportment (eg Cd, Sb, As, etc)
  Predict where metals are concentrated and liberated
  mineralogy: sulfide species

## Slide 25: Modelling geology and grade
Ore grade
SG
Tonnage
Value
Knight et al., 2011

## Slide 26: Resource-calculated ore with problematic Cd, As, Sb contents
Is it still “ore”?
Knight et al.

## Slide 27
Stable Landforms and Sustainable Substrates
Effective store-release cover design for containment of waste
Remediation of problematic soil conditions, Yarraman mine
Options and strategies for tailings revegetation
Organic matter in mine rehabilitation and the carbon balance

## Slide 28: Water and contaminants in the landscape
Geochemistry of mine water in monsoonal climates
Lead pathways study
Acid mine drainage and geochemistry, Croydon Mine
Rehabilitation of oilfield brine impacts in an arid environment

## Slide 29: Ecosystem Structure and Function
Restoration of brigalow plant communities on degraded landscapes
Potential impacts of subsidence on the Newness Plateau, Centennial Coal
Long-term monitoring and research strategies at North Stradbroke Island
Sustainability of koala populations in mining environments

## Slide 30: Monitoring and Mapping Technologies
SPOTing long-term changes in vegetation over short-term variability
Surface conditions of swamps subject to subsidence with high-resolution imagery
Mapping and validation of strategic cropping land
Spatial and temporal modelling for vegetation monitoring uncertainty

## Slide 31: Mine closure and end-use planning
Closure strategy for tailings storage facilities
Risk assessment tools for post-mined line
Pre-operational rehabilitation research
Early ore body characterisation for the prediction of acid and metalliferous drainage

## Slide 32: Mine closure and end-use planning
Closure strategy for tailings storage facilities
Risk assessment tools for post-mined line
Pre-operational rehabilitation research
Early ore body characterisation for the prediction of acid and metalliferous drainage

## Slide 33
Same approach as for processing:
  Understand the mineralogical and geological relationships
  Locking, exposure to fluids, element deportment, bio-availability
Notes: 33

## Slide 34: Mineral variability

## Slide 35: Prediction via mineral characterization

## Slide 38
Before remediation ll After remediation

## Slide 39
Brownfields
SEE
LOM/Long Term
Planning
Short Term Planning
Scheduling
Sustainability & Extraction
Efficiency
Application
SEE Lite
Greenfields
LOM/Long Term
Planning

## Slide 40: SEE: Sustainable extraction efficiency
Historical Mine to Mill Results
  cross-discipline (blast to S/AG Mill) intervention
  increases mill throughput in the short term
Geology-Mine-Plant Integration
  fully integrated predictive optimisation process
  considers key eco-efficiency attributes
  enables long-term improvements
- Metal tonnes - Cost ($/tonne) - Total Energy (kWh/tonne)
- Water (Ml/tonne) - Carbon Emissions (CO2/tonne)

## Slide 41: Putting it together
GeoMet Model

## Slide 42: Energy impact
kWh/t
% recovery
Flexible Circuits
Notes: Total with embodied = incl energy to make grinding media
Win win
Requires planning and flexibility

## Slide 43
More effective project management

## Slide 44: Impacting the cash flow
This illustrates the difference in cash flow predicted from a fully attributed GeM mine planning model versus the mines traditional ore reserve model. The variation is up to $50m per annum. This information leads to informed rescheduling to maximise value and minimise risk.
Uneconomic ore impacting cash flow

## Slide 45: Predict …. Plan …. Manage
PREDICT process performance
Recognize variability and geological drivers
Model relationships among attributes
Interpolate throughout mineral deposit
PLAN proactively
Integrate into mine plan and scheduling
Reduce uncertainty
Improve performance
MANAGE impacts
Understand and control environmental consequences
Reduce overall project risk
Recognize financial value through NPV and IRR options

## Slide 46: Life-of-mine geomet application
Value
Locked in variable ore relationships
Team-based approach
Integrate data sets
Operating cost reduction
Risk mitigation
through life of project
Mineralogy
Closure
Reclamation
Drilling
Core logging
Geochemistry
Assay
Materials
Attributes
Metallurgical
tests
Mine plan and
design
Operations
QA/QC
Piloting
Geological model
Characterisation
data sets
$ value